## Slide 1: Fibonacci Series generator Using Logisim
By Logicaliants

## Slide 2: Group Members
Kariem Alaa-Eldien Soliman (61)
Mahmoud Ahmed Elsayed (83)
Mohamed Sherief Mohamed (69)
Omar Shaaban Rabea (56)
Mahmoud Khalid Sayed (84)

## Slide 3: Objectives:
  Learning how to work with Logisim Simulator
  Team work
  Handling Inputs & Outputs of different Components

## Slide 4: Components (1/2):
  3 Registers for A, B and C variables
  Controlled Buffers
  S-R Flip - Flop
  Pull Resistor
  Probe
  De – Multiplexer
  Counter

## Slide 5: Components (2/2):
  8. Clock Generator
  9. Sum Logic Gates like AND & NOR gates
  10. Push Button
  11. 32 –bit Adder

## Slide 6: What is Fibonacci Series ?
  Fibonacci numbers are part of a sequence in which every term is equal to the sum of the previous two terms starting with the numbers 0 and 1 we add those together to get 1 then add 1 plus 1 to get 2 then 1 plus 2 is 3 2 plus 3 is 5 3 + 5 is 8 and so on.
  I wrote a program in Python which generates Fibonacci numbers.

## Slide 7: Python Code :
  def fibgen (n):
  A , B , C = 0 , 1 , 1
  for i in range (0 , n):
  print (A , sep = " , ")
  C , A , B = A+B , B , C
  fibgen (10) # END
  Output : 0 , 1 , 1 , 2 , 3 , 5 , 8 , 13 , 21 , 34

## Slide 8: Screenshot of Manual Fib. Generator:

## Slide 9: Screenshot of auto Fib. Generator:

## Slide 10: Description :
First what you need is a full adder, made from gates. Second thing you need are three registers A, B and C. A and B are on the inputs to the Adder, C is on the output. Each register needs a control wire that lets you update its contents.
At the beginning, you need to set A to 0 and B to 1. {In each cycle you take the output of the adder and put it into C, then in next step transfer the contents from A to B and from C to A.} Repeat for so many cycles to get to your desired fibonacci number.

## Slide 11: Notes :
Buffers must be used to avoid conflicting of input signals.
Only one of two De - Mux must be active at a time.
Two buffers used for B - Register to handle its input :
  Initially, it gets the value of constant 1.
  Then, it gets the value of C – Register for the rest of whole program.
  # END_OF_PRESENTATION